INVITATION FOR QUOTATION

TEQIP-III/2018/ntst/Shopping/36				                       11-Jan-2019

To,

____________________________

__________________________________

______________________________________

______________________________________

Sub: Invitation for Quotations for supply of Goods

Dear Sir,

- You are invited to submit your most competitive quotation for the following goods with item wise detailed specifications given at Annexure I,

| Sr. No | Brief Description | Quantity | Delivery Period(In days) | Place of Delivery | Installation Requirement (if any) |
| --- | --- | --- | --- | --- | --- |
| 1 | Production Engineering laboratory -2 | 1 | 30 | National institute of Technology, Sikkim: Ravangla-737139, South Sikkim, Sikkim, India | Yes Mandatory |

- Government of India has received a credit from the International Development Association (IDA) towards the cost of the Technical Education Quality Improvement Programme[TEQIP]-Phase III Project and intends to apply part of the proceeds of this credit to eligible payments under the contract for which this invitation for quotations is issued.

- Quotation,

  - The contract shall be for the full quantity as described above.

  - Corrections, if any, shall be made by crossing out, initialing, dating and re writing.

  - All duties and other levies payable by the supplier under the contract shall be included in the unit price.

  - Applicable taxes shall be quoted separately for all items.

  - The prices quoted by the bidder shall be fixed for the duration of the contract and shall not be subject to adjustment on any account.

  - The Prices should be quoted in Indian Rupees only.

- Each bidder shall submit only one quotation.

- Quotation shall remain valid for a period not less than 45 days after the last date of quotation submission.

- Evaluation of Quotations,

The Purchaser will evaluate and compare the quotations determined to be substantially responsive i.e. which

  - are properly signed ; and

  - confirm to the terms and conditions, and specifications.

- The Quotations would be evaluated for all items together.

- Award of contract:

The Purchaser will award the contract to the bidder whose quotation has been determined to be substantially responsive and who has offered the lowest evaluated quotation price.

  - Notwithstanding the above, the Purchaser reserves the right to accept or reject any quotations and to cancel the bidding process and reject all quotations at any time prior to the award of contract.

  - The bidder whose bid is accepted will be notified of the award of contract by the Purchaser prior to expiration of the quotation validity period. The terms of the accepted offer shall be incorporated in the purchase order.

- Payment shall be made in Indian Rupees as follows:

Delivery and Installation - 80% of total cost Satisfactory Acceptance - 20% of total cost

Annexure I

| Sr. No | Item Name | Specifications |
| --- | --- | --- |
| 1 | Production Engineering laboratory -2 | CNC Vertical Milling Machining Quantity: 1 (Brand/ Make: i.HMT, ii. HASS, iii. EMCO, iv. DECKLMAHO or Equivalent) Description/ Specification: - 20 Station tool magazine - AC Servo Axes Drive ( Fanuc make ) - Ball screw stretching for X, Y & Z Axes - Chip disposal to the rear side of the machine through two chutes on the sides - CNC System Fanuc 0i-MF with 10.4” Colour LCD - Coolant tank with chip tray - Fail safe brake for vertical axis (Z-Axis) - Flexible coupling for X, Y & Z Axes - LM Guide ways for X, Y & Z Axes - Manual Pulse Generator - One set of manuals - Panel cooler for electrical cabinet - Rapid traverse of 30 / 30 / 30 m/min. for X, Y & Z Axes - Rigid tapping - Smart Feature – Machine Connect™ (OEM) - Spindle nose taper 7/24 No.40 - Spindle power (Fanuc Make) 15 Min./Cont. Rating - 11 / 7.5 KW - Spindle speed of 60 - 6000 rpm (Indirect drive) - Standard CNC features of Fanuc 0i-MF with Colour LCD - Standard Worklight - Three tier indication lamp - Tool life management - Tool shank BT - 40 - Total Machine Enclosure - Twin Arm (Random) type High Speed Auto Tool Changer - Flood Coolant System around the Spindle - Chip flushing system on the base - Full packing for basic machine. - Coolant gun Technical Specification: Description Specification TABLE Table size Not less than 1000 x 450 mm T-slot dimension (N x W x P) Not less than 4 x 18 x 100 Max. load on table Not less than 400 mm Dist. from floor to table top Not less than 925 mm MACHINE CAPACITY X - Axis Travel Not less than 800-850 mm Y - Axis Travel Not less than 450-500 mm Z - Axis Travel Not less than 500-550 mm Dist. from spindle face to table top Not less than 175 – 675 mm Dist. from spindle center to column guide ways Not less than 510 mm Coolant supply - through flexinox hoses Not less than 20 lpm SPINDLE Spindle nose taper 7 / 24 No.30 Spindle speed - indirect drive (std.) Minimum 60 – 6000 rpm Spindle bearing dia. Minimum 70 mm FEED Rapid traverse x, y & z axes Not less than 30 / 30 / 30 m/min. Cutting feed Not less than 1 – 10000 mm/min Guide ways for X, Y & Z axes Linear Motion AUTOMATIC TOOL CHANGER Number of tools Minimum 20 Nos. Max. tool dia. Minimum 80 mm Max. tool dia. With adjacent pockets empty Minimum 155 mm Tool selection Bi - Directional Tool length max. Not less than 250 mm Tool weight max. Not less than 8 kg Chip to chip time 4.5 Sec. Tool change system Twin Arm Tool shank type BT-40 Pull stud type MAS-403 ACCURACY WITH ROTARY ENCODER Positioning for x, y & z axes as per ISO 230-2 0.010 mm Repeatability for x, y & z axes as per ISO 230-2 ± 0.003 mm MOTORS Spindle power (continuous) 7.5/11 kw or higher Feed motor X, Y & Z axes 12 / 12 / 20 Nm or higher MISCELLANEOUS Machine width 2200 mm Machine depth 3100 mm Machine height 2550 mm Machine weight – net Not Less than 5300 KG Input Power supply for basic machine 25 KVA Pneumatic pressure required 5 Kgf / Cm2 TANK CAPACITY Coolant tank 300 liter minimum. Lubrication tank 3 min. Machine Features / Accessories - Standard Panel Cooler For Electrical Cabinet Fail Safe Brake For Z – Axis Standard Work Light Coolant Tank & Chip Tray Three Tier Indication Lamp To Indicate Cycle Running Ready For Next Cycle & Machine In Alarm Status Flexible Coupling For X, Y & Z Axes Manual Pulse Generator Rigid Tapping Total Machine Enclosure Chip Disposal To The Rear Side Of The Machine Through Two Chutes On The Sides Manuals - One Set Ball Screw Stretching For X,Y & Z Axes Tool Life Management Machine Connect Coolant gun Flood coolant system around the spindle Chip flushing system on the base Full packing for basic machine Inverter Based Pulse TIG DC Welder Quantity: 1 (Brand/ Make: i. ADOR , ii. ESAB, iii. OERLIKON, iv.GYS, v. REHM or Equivalent) Description/ Specification: Three phase inverter based, high frequency and high power factor Pulse TIG/MMA DC Welder Useful for wide variety of material types and thickness Full featured TIG controls possible. HF ignition. Intelligent protection: over/ under voltage, over current/temperature Water cooled torch with cooling unit option. Latest PWM inverter technology. High efficiency (>85%) Smooth and stable arc with spatter less welding. Pulse TIG for precision welding Technical Details: Input: Input voltage: 415V,+15%,-10% Phase : Three(3) Frequency: 50/60Hz Efficiency@100%duty cycle: 85% Power factor@100%duty cycle: 0.94 max. Max Input @100% duty cycle: MMA Mode: 13KVA TIG Mode : 10 KVA Max Input @No load: MMA Mode: 0.13 KVA TIG Mode : 0.13 KVA Output: Open circuit voltage: 70V Welding current range: MMA Mode: 50-400A TIG Mode : 10-400A Welding current@ 100% Duty Cycle: 310A @60% Duty Cycle:400A Pulse TIG Parameters Duty ratio: 10-90% Pulse frequency:0.5-10Hz Base current: 10-90% of Ipulse Current Pulse current: 10-400A Start current: 10-400A Current unslope time: 0-10sec Current down slope control: 0-10sec Pre-flow:0-5sec Post flow:0.1-20sec Crater current: 10-400A Current/Voltage Display: 7 Segment LED display for current &other parameter Ingress protection: IP23 Class Cooling: Forced Air Insulation: H Welding Output Terminals: Cam Lock Connections Length: 660mm Width: 315mm Height: 485mm Weight: 46kg Water Cooling Unit Input supply voltage(AC): 230V Phase : 1 Frequency: 50/60Hz Water reservoirs: 8 Ltrs Flow rate: 10Ltr/Min Inverter based MIG Welding Quantity: 1 (Brand/ Make: i. ADOR, ii. ESAB, iii. OERLIKON, iv.GYS, v. REHM or Equivalent) Description/ Specification: Inverter based digitally controlled GMAW outfit High efficiency and high power factor- resulting energy saving Enhanced reliability due to SMD technology Auto “Weld Stop” when welding torch is taken away from weld job Compatible to Power Generator Supply Digital panel for adjusting the welding parameters 25% more energy efficient than conventional machines Maximum power factor is 0.93 Excellent dynamic response enables superior arc characteristics 2T, 4T operating modes Electronic choke adjustment for better arc control Crater voltage and crater current adjustment through digital panel Unique feature of Fresh Tip Transfer(FTT) to avoid globule formation Automatic “Weldstop “ facility Protection: The equipment is provided with following protections. Under voltage and Over Voltage: Error message is displayed and the equipment shuts down if the Over temperature: Error message is displayed and the equipment shuts down if the temperature of the main power components exceeds the safe limits. Single phasing protection: Error message is displayed and the equipment shuts down if any one of the three phase supply line is absent (single-phasing prevention / protection) Power Source Specifications: Input: Input voltage: 415V,+15%,-10% Phase : Three(3)Φ Frequency: 50/60Hz Input @100% duty cycle : 12KVA @No load : 0.24 KVA Output: Open circuit voltage: 65V±5% Welding current range: 50-400A Welding current@ 100% Duty Cycle: 400A @60% Duty Cycle:310A Welding Voltage Range: 16-39V Crater current Range: 50-400A Crater Voltage Range: 16-39V Mode of operation: 2 track, 4 track, Gas check, OCV check facility Remote control available for setting voltage and current Power factor: max 0.93 Efficiency: 87%@ 100% duty cycle Ingress protection: Class IP23 Cooling: Forced Air Insulation: H Length:700mm Width: 450mm Height: 600mm Weight: 44kg Audio Noise Emission: 70dB Wire Feeder Specifications Wire feed speed: 1.5-18m/min Suitable welding wire Aluminum: 1.2- 1.6 diameter : Steel:0.8, 1.0,1.2,&1.6 Wire Roll Drive : Four Wire drive motor: permanent magnet DC Wire Feeder Motor Voltage: 42V Wire Feeder Fitted with Rollers : 1.2/1.6 for solid wire 2 no. Wire spool capacity : 15kg Length:563mm Width: 230mm Height: 410mm Weight(without Spool): 16kg Torch Specifications: Rating: 400A @60% Duty Cycle for CO2 End Connection To Torch: Euro Suitable For Wire: 0.8, 1.0, 1.2, 1.6 Torch length: 3m Horizontal Spindle Surface Grinding Machine Quantity: 1 (Brand/ make: i. PHILIPS CROP, ii. KEHEREN, iii. HMT, iv. CHEVALIERMACHINERY or Equivalent) Description/ Specification: Table size: 600 X 300 mm Table movement motorized Max longitudinal travel : 625mm Cross wise travel: 315mm Hand wheel per / rev. 100 mm (4”), Motorized cross maximum 262 mm Auto transverse increment 1-10mm Hand wheel per / rev. 5mm Hand wheel per graduation 0.02mm Manual vertical movement 400mm Hand wheel per / rev. 1mm Hand wheel per graduation 0.01mm Grinding spindle drive 1 HP 415 V 2800 RPM Table drive motor 1 HP 415 V 1500 rpm Complete with electrical, grinding wheel, wheel flange, flange puller, magnetic chuck setting screw, diamond dresser block, spindle locking spanner, coolant pump with tank & spout assembly, close pole magnetic chuck 20”x12”, machine lamp |

FORMAT FOR QUOTATION SUBMISSION

(In letterhead of the supplier with seal)

Date: _______________

To:

____________________________

____________________________

| Sl. No. | Description of goods (with full Specifications) | Qty. | Unit | Quoted Unit rate in Rs. (Including Ex Factory price, excise duty, packing and forwarding, transportation, insurance, other local costs incidental to delivery and warranty/ guaranty commitments) | Total Price (A) | Sales tax and other taxes payable |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | In % | In figures (B) |
| Total Cost |  |  |  |

Gross Total Cost (A+B): Rs. ________________

We agree to supply the above goods in accordance with the technical specifications for a total contract price of Rs. ———————— (Amount in figures) (Rupees ————————amount in words) within the period specified in the Invitation for Quotations.

We confirm that the normal commercial warranty/ guarantee of ——————— months shall apply to the offered items and we also confirm to agree with terms and conditions as mentioned in the Invitation Letter.

We hereby certify that we have taken steps to ensure that no person acting for us or on our behalf will engage in bribery.

Signature of Supplier

Name: __________________

Address: __________________

Contact No: ______________