INVITATION FOR QUOTATION

TEQIP-III/2018/ntst/Shopping/35				           11-Jan- 2019

To,

_________________________________

_______________________________________

_______________________________________

___________________________________________

Sub: Invitation for Quotations for supply of Goods

Dear Sir,

- You are invited to submit your most competitive quotation for the following goods with item wise detailed specifications given at Annexure I,

| Sr. No | Brief Description | Quantity | Delivery Period(In days) | Place of Delivery | Installation Requirement (if any) |
| --- | --- | --- | --- | --- | --- |
| 1 | Items for Production Engineering Laboratory-1 | 1 | 30 | National Institute of Technology Sikkim: Ravangla-737139, South Sikkim, Sikkim, India | Mandatory |

- Government of India has received a credit from the International Development Association (IDA) towards the cost of the Technical Education Quality Improvement Programme [TEQIP]-Phase III Project and intends to apply part of the proceeds of this credit to eligible payments under the contract for which this invitation for quotations is issued.

- Quotation,

  - The contract shall be for the full quantity as described above.

  - Corrections, if any, shall be made by crossing out, initialing, dating and re writing.

  - All duties and other levies payable by the supplier under the contract shall be included in the unit price.

  - Applicable taxes shall be quoted separately for all items.

  - The prices quoted by the bidder shall be fixed for the duration of the contract and shall not be subject to adjustment on any account.

  - The Prices should be quoted in Indian Rupees only.

- Each bidder shall submit only one quotation.

- Quotation shall remain valid for a period not less than 45 days after the last date of quotation submission.

- Evaluation of Quotations,

The Purchaser will evaluate and compare the quotations determined to be substantially responsive i.e. which

  - are properly signed ; and

  - confirm to the terms and conditions, and specifications.

- The Quotations would be evaluated for all items together.

- Award of contract:

The Purchaser will award the contract to the bidder whose quotation has been determined to be substantially responsive and who has offered the lowest evaluated quotation price.

  - Notwithstanding the above, the Purchaser reserves the right to accept or reject any quotations and to cancel the bidding process and reject all quotations at any time prior to the award of contract.

  - The bidder whose bid is accepted will be notified of the award of contract by the Purchaser prior to expiration of the quotation validity period. The terms of the accepted offer shall be incorporated in the purchase order.

- Payment shall be made in Indian Rupees as follows:

Delivery and Installation - 80% of total cost Satisfactory Acceptance - 20% of total cost

Annexure I

| Sr. No | Item Name | Specifications |
| --- | --- | --- |
| 1 | Items for Production Engineering Laboratory-1 | Precision Conventional Lathe Quantity: 1 (Preferred Brand/ Make: i. Kirloskar, ii. HMT, iii. Bhaviya Machine tools, iv. PANTHER or Equivalent) Description/ Specification: Height of Centers: 250 Tool Shank Section: 25 X 25 mm Feed Longitudinal: 60/0.08-1 Feed Transverse: 60/0.02-0.25 Metric Thread: 40/0.4-7 mm Thread Per Inch: 45/70-4 TPI Lead Screw: 6 mm Main Motor: 3.7 KW / 5 HP Admit Between Center: 1500 Quill Dia. / Travel: 75/150 Tail Stock Sleeve: MT – 4 Top Slide Travel: 150 Swing Over Bed: 500 Swing Over Slide: 290 Width Of Bed: 325 Spindle Bore: 80 Spindle Nose: LO Type Spindle Speed No.: 16 H-L RPM: 30-1550 Cross Slide Travel: 260 Parts should be available: Electrical Motor 5 HP, Chuck Plate, True Chuck, Dog Chuck, Steady Rest, Coolant Fitting Conventional, Taper Turnnig Attachment, Grinding Fitting, Revolving Center Accessories to be provided: Center Adopter, Dead Center, Thread Dial Indicator, Change Gear, Motor Stand, V Belt, Motor Pully, Spanner Set, Chip Collector Tray, Vibration Pads, Foundation Bolt, First Fill Oil, Manual Book, Wheel & Handle Set, Clutch Stick with Knob, Quick Change Tool Post, Chuck Plate, Switch Stand, Chuck Spanner, Eye Protector Glass, Tool Bag, Colour Can, Apron, Machine Lamp, Carriage Stopper. CNC Lathe Machine Quantity: 1 (Preferred Brand/ Make: i. LMW, ii. ACE, iii. EMCO, iv.BFW, v. HASS or Equivalent) Description/ Specification: 3 Jaw power operated hollow high speed chuck nominal Ø200mm including power chucking cylinder and accumulator. (Recommended max. speed 3500 rpm) (Bar Capacity: Ø 42 mm max.) Note: Metric serration (1.5mm x 60°) is standard. - 8 station Bi-directional turret (BTP-80) with wedge type OD tool clamping - A2-6 Spindle (Cartridge) - AC Servo Axes Drives (`Fanuc' make) - AC Spindle Drive (`Fanuc' make) - Air condition unit for control cabinet (Panel mounted type) (Model : IGLOO; Ace make) - Automatic Centralised Oil Lubrication System - Basic Hydraulic System with Drain line Oil cooler - Built-in lighting system - Controls: Fanuc Oi – TF - Coolant System - Drain line Oil cooler - Electronic hand wheel (MPG) (make: Fanuc) - Hardened & Ground Box type Steel Guideways - Machine ‘Ball Bar’ calibrated - Machine Axes (X&Z) laser calibrated for high positioning accuracy and repeatability - Machine Colour: RAL 7022 (Umbra Grey), RAL 9010 (Pure White) and RAL 1028 (Melon Yellow) - One set of machine manuals (Instruction manual and Parts manual) along with 01 no. CD - Oriented Spindle Stop (M19 Command) - Packing - Programmable quill - Smart Feature – Machine Connect™ (OEM) - Spindle Motor Power: 11 kW 15 mins. Rating / 7.5 kW continuous rating - Spindle Speed: 50 – 3500 rpm (Subject to work holding selection) - Standard tooling package as per Annexure - II and with all other standard features - Tailstock with external rotating centre - Three Colour Machine status lamp Technical Specification: Description Specification Work Area Swing over Bed Not less than 500 mm Swing over carriage Not less than 260 mm Distance Between Centres Not less than 550 mm Turning Diameter Not less than 350 mm Turning Length Not less than 500 mm Traverse X Axis Travel Not less than 180 mm Z Axis Travel Not less than 500 mm Main spindle Spindle Nose A2-6 or better Spindle Bore Not less than 63 mm Chuck Size 200 mm Spindle Drive Spindle Motor rated power (Continuous / 15 Min.) 7.5 / 11 kw Spindle Speed ≥3000 rpm Automatic Tool Turret Number of tool stations 8 Stations Maximum Boring Bar Dia. Not less than 40 mm Tool Cross Section 25 mm x 25 mm Turret type BTP-80 Tailstock Tailstock base travel Minimum 235 mm Quill Diameter Not less than 80 mm Quill Stroke Not less than 100 mm Taper of Quill MT 4 Control System Controller Fanuc 32 bit processor preferable 64 bit RISC processor 2 axes simultaneous controllable 8.4"TFT colour monitor with soft keys Feed System Rapid Traverse X-Axis 20 m / min Rapid Traverse Z-Axis 20 m / min Axis Drives & Control Digital controlled drive & motors for all axes Oversized ball screws nuts and spindle 32 mm dia. screws with min 10mm pitch, C3 class or better Ball Screws arrangement should be fixed and supported at both end General Machine Weight Not Less than 4000 Kg Machine overall Dimension (L x W x H) Minimum 2540 x 1785 x 2050 mm Standard Features Electronic hand wheel (MPG) Machine Lamp AC unit for electrical panel Coolant system Built in lighting system Machine operating and programming manual 1 set Installation, maintenance and spare part manual 1 set Training to faculty on operation and maintenance for a duration of 4 to 5 days Automatic Centralized lubrication All Geared Shaping Machine Quantity: 1 (Preferred Brand/ make: i. Kirloskar, ii. HMT, iii. Bharat Machinery, iv. Bhaviya Machine tools or Equivalent) Description/ Specification: Length of Stroke 30” (762 mm) Length of Ram 1410 mm Length of Width Ram Baring : 1020x330 Distance from Table to Ram: 510/75 Working Surface of the table 762 x 390 mm Maximum Table Travel Horizontal 787 mm Maximum Table Travel Vertical 450 mm Maximum Travel of Tool Slide 203 mm No. of Speed 4. Range 8,16,32,48 Table Feed Per Stroke of Ram 0.22 mm inbuilt lubrication tank, that is, the machine lubricates itself on operation, Swivel Type table +/- 90°, Tool Slide Swivel +/- 60°, complete with standard accessories consisting of Swivel Base Shaping Vice, Motor Pulley and Table Lifting Handle, 5 HP 415 V 50 Hz 1500 RPM Motor with DOL starter Keyway cutting attachment Tool lifting device Feed to the tool slide Allen key set V belt Screw driver Spanner set, Oil can Tool box Electric motor & starter |

FORMAT FOR QUOTATION SUBMISSION

(In letterhead of the supplier with seal)

Date: _______________

To:

____________________________

____________________________

| Sl. No. | Description of goods (with full Specifications) | Qty. | Unit | Quoted Unit rate in Rs. (Including Ex Factory price, excise duty, packing and forwarding, transportation, insurance, other local costs incidental to delivery and warranty/ guaranty commitments) | Total Price (A) | Sales tax and other taxes payable |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | In % | In figures (B) |
| Total Cost |  |  |  |

Gross Total Cost (A+B): Rs. ________________

We agree to supply the above goods in accordance with the technical specifications for a total contract price of Rs. ———————— (Amount in figures) (Rupees ————————amount in words) within the period specified in the Invitation for Quotations.

We confirm that the normal commercial warranty/ guarantee of ——————— months shall apply to the offered items and we also confirm to agree with terms and conditions as mentioned in the Invitation Letter.

We hereby certify that we have taken steps to ensure that no person acting for us or on our behalf will engage in bribery.

Signature of Supplier

Name: __________________

Address: __________________

Contact No: ______________